## Slide 1: Introduction to Risk Management
C7 Slide <number>
Notes: INTRODUCTION TO RISK MANAGEMENT:
SLIDE 1 of 1: INTRODUCTION (1 min)
Risk management should be seen as a fundamental preventative measure to support safe conventional ammunition stockpile management.
The more complete the knowledge is on the risk presented by the ammunition and explosives, the better the decisions can be regarding the likelihood and the consequences of an explosive event.
The term ‘explosive event’ refers to an unexpected and undesired initiation of an explosive substance or article within an ammunition depot leading to significant or catastrophic consequences.
<number>

## Slide 2: The Concept of Safety
‘Safety’ refers to the reduction of risk to a tolerable level
Risk = Likelihood x Consequence
‘Tolerable risk’ refers to the risk that is accepted in a given context based on the current values of society
C7 Slide <number>
Notes: CONCEPT OF SAFETY:
SLIDE 1 of 1: THE CONCEPT OF SAFETY (3 min)
Whatever industry or sphere we are in, there will never be any such thing as something that is 'totally safe'. There will always be some element of risk, even if we have done everything that seems within our power to prevent any risk.
The risk left after our efforts to make things 'safer' is the residual risk.
What is risk? Risk is defined as “Risk = Likelihood x Consequence”
The important thing is to get this residual risk to an 'acceptable' level. Of course, the logical question here is what is acceptable. IATG states that acceptable, in this context, is 'tolerable risk'.
Within IATG, tolerable risk is defined as "The risk that is accepted in a given context based on the current values of society"
This leads us to the definition of ‘safety’. Within IATG, the term ‘safety’ refers to the reduction of risk to a tolerable level.
How does this apply to us?
In the context of conventional ammunition stockpile management, the enabling processes of storage, handling, destruction, etc, can never be absolutely safe; they can only be relatively safe. This is an inevitable fact of life, which does not mean that all efforts to ensure safety are not being made. It just means that it cannot be proved, with 100% confidence, that absolute safety is being achieved.
The risk management systems recommended in IATG, and used within the IATG software, aim to be as close to that 100% ideal confidence level as is realistically possible, whilst allowing stockpile management organisations to determine what is the tolerable risk that they are prepared to accept in their particular environments.
The techniques covered, or referred to, in IATG 02:10 should be applied in order to manage the risks of conventional ammunition stockpile management.
<number>

## Slide 3: Introduction to The Risk Management Process
Risk management: a huge, wide ranging topic
IATG provides more detail
As well as processes, look to create a safety culture as well as:
  A Reporting Culture
  A Just Culture
  A Flexible Culture
  A Learning Culture
  A Questioning Culture
C7 Slide <number>
Notes: THE RISK MANAGEMENT PROCESS: (5 slides, 14 min)
SLIDE 1 of 5: INTRODUCTION TO THE RISK MANAGEMENT PROCESS (4 min)
Risk management is a complex process which we simply cannot cover in full in this lesson. You will not become a safety management practitioner by sitting here for the next 45 minutes. However, the aim is really to introduce you to the concepts of risk management so that you have a basic awareness and appreciation of this huge topic for when you study more detailed, specific processes later in the course. The IATG provide more detail on the generic risk management process and you should study this and refer to this.
Remember though that we are trying to achieve real improvements in safety ‘on the ground’, rather than just going through a number of paperwork processes because the instructions say that we have to. There is no point in doing procedural ‘tick box exercises’. You must actually think about this and be alert and aware of safety, and look to achieve real safety. The processes in the IATG are tools to allow us to improve safety. But you, and your colleagues and others, must ensure that you are safe in your work and activities. In essence there needs to be a sound environment – a culture – within the organisation that treats people fairly, even if they have made mistakes. There needs to be a fair, honest reporting culture. Indeed, this is all part of a higher level “Safety Culture” which must be seen as desirable and is worth creating.
A safety culture may be seen as being based on 5 key elements:
A Reporting Culture
A Just Culture
A Flexible Culture
A Learning Culture
A Questioning Culture
This may be a big cultural leap for some entities, however development of a safety culture should certainly aide a safer and more responsible environment. This 5-element model comes from the Haddon-Cave Nimrod Report for the UK MOD, 2009.
<number>

## Slide 4: The Risk Management Process
‘Risk management’ refers to the complete risk-based decision-making process and comprises:
  Risk assessment
  Risk analysis
  Risk and ALARP evaluation
  Hazard Identification
  Hazard Analysis
  Risk estimation
  Risk reduction
  Risk acceptance
  Risk communication
C7 Slide <number>
Notes: THE RISK MANAGEMENT PROCESS: (5 slides, 14 min)
SLIDE 2 of 5: THE RISK MANAGEMENT PROCESS (3 min)
Within IATG, the term ‘risk management’ refers to the complete risk-based decision-making process.
The components of risk management are:
Risk assessment
Risk analysis
Risk and ALARP evaluation. Note here that ‘ALARP’ is a commonly used abbreviation in safety management and it stands for ‘As Low As Reasonably Practicable’.
Hazard Identification
Hazard Analysis
Risk estimation
Risk reduction
Risk acceptance
Risk communication
We will look at how these interact with each shortly.
<number>

## Slide 5: The Risk Management Process
C7 Slide <number>
Notes: THE RISK MANAGEMENT PROCESS: (5 slides, 14 min)
SLIDE 3 of 5: THE RISK MANAGEMENT PROCESS (1 min)
Within our risk management, we need to define we deem to be ‘tolerable risk’ and ‘ALARP’.
How does this apply in real life?
IATG offers detail on deriving acceptable levels of risk in terms of probability (or likelihood) for different groups of people, for example.
It may be determined at the highest levels that military members of staff who work in the ammunition depot must not be subjected to an accident, for which there is a probability of more than one in a million.
<number>

## Slide 6: Hypothetical Example
Tolerable Risk and ALARP - An example:
Acceptable level of risk = 1 x 10-6 (one in a million)
Risk level is now 1 x 10-3 (one in a thousand=unacceptable)
…so we put some form of mitigation in place, and then we determine that…
The mitigated risk level becomes 1 x 10-6
C7 Slide <number>
Notes: THE RISK MANAGEMENT PROCESS: (5 slides, 14 min)
SLIDE 4 of 5: HYPOTHETICAL EXAMPLE (3 min)
(Instructor: text on the slide appears on the click of a mouse, so click mouse when instructed in the text below. Note that the final action on this slide needs 2 clicks to turn it over to the next part of the slide sequence).
On the screen we have a hypothetical example, which could be for any particular hazard:
(CLICK) Note here that one in a million is written mathematically as 1 x 10-6.
The pre-determined probability of an event happening – which his considered to be acceptable by the ‘powers that be’ – is one in a million.
(CLICK) However having done the risk and ALARP evaluation we decide that the actual risk at the moment of that occurring is one in a thousand. This is much more likely than we want.
(CLICK) So we come up with some mitigation measures, and these reduce the probability right down, to the point where it becomes one in a million chance of that risk occurring.
(CLICK) The mitigated risk now becomes one in a million.
(CLICK until slide turns over)
<number>

## Slide 7: Hypothetical Example
Tolerable Risk and ALARP - An example:
Tolerable level of risk = 1 x 10-6 (one in a million)
Risk level is now 1 x 10-3 (one in a thousand=unacceptable)
…so we put some form of mitigation in place, and then we determine that…
The mitigated risk level becomes 1 x 10-6
Which meets the tolerability requirement
C7 Slide <number>
Notes: THE RISK MANAGEMENT PROCESS: (5 slides, 14 min)
SLIDE 5 of 5: HYPOTHETICAL EXAMPLE (3 min)
(Instructor: text on the slide appears on the click of a mouse, so click mouse when instructed in the text below).
(CLICK) Based on this, the mitigated risk is now tolerable because it meets the pre-determined target.
Note that if, for some reason, the mitigation measures failed or were removed, the probability would increase and this risk would no longer remain as tolerable. Action would be required to reinstall the mitigation measures.
In ‘real life’ then for us, we could be talking about the risk of death to a depot worker because of ammunition pallets that are too highly stacked. Lets say in our depots that they are usually stacked 5 pallets high.
If the stack topples over, the worker would be killed.
The pre-determined target for keeping the worker from dying is a probability (or a ‘chance’) of 1 in a million.
However lets say that we find out, through research of health and safety data about warehouses, that the risk of pallets falling over when they are stacked 5 high is 1 in a thousand. This is too high a risk for our workers.
We then find out through researching the same data that the risk of a stack toppling over is only 1 in a million if they are stacked 3 high.
So we implement a regulation that forbids the stacking of pallets over 3 high. This is a reasonably achievable, practical mitigation measure. We communicate this new regulation to the depot foremen, and we ensure that they understand this and they make sure that pallets are only stacked 3 high.
The risk therefore comes down to 1 in a million, which meets our pre-determined target and is therefore considered to be tolerable.
Tolerable risk is determined by the search for absolute safety contrasted against factors such as:
a) the inherent explosive safety hazards of storing, handling and processing ammunition;
b) available resources;
c) the conventions of the society where the ammunition is being stored; and
d) the financial costs.
This determination aides us in assessing whether risks are ALARP. The key factor here of course is 'practicable'.
<number>

## Slide 8: Qualitative v Quantitative Risk Assessments
Qualitative:
Descriptive
Quantitative
Measurable
or
Calculable
C7 Slide <number>
Notes: QUALITATIVE RISK ASSESSMENTS: (1 slides, 5 min)
SLIDE 1 of 1: QUALITATIVE v QUANTATITIVE RISK ASSESSMENTS (3 min)
The difference:
Qualitative risk assessments are descriptive.
Quantitative risk assessments use measurable or calculable data.
This is relatively easy to remember: Quantitative assessment uses actual quantities – ie figures. Qualitative assessment is a quality judgement.
Qualitative Risk Assessments:
Qualitative risk assessments are by far the most widely used approach to risk analysis in many circumstances. Probability data is not required as an estimate of potential loss is used.
They should be rarely used during conventional ammunition storage risk assessment processes in terms of explosive safety distances and the like, as there are a range of scientifically accepted and proven techniques available to allow for a more quantitative risk assessment.
They may be used though for specific processes that support ammunition management where little quantitative data is available. For example there is little quantitative data for tasks such as ammunition processing tasks. In this kind of case, qualitative assessment may be the only workable way of assessing risk.
Quantitative Risk Assessment:
Quantitative Risk Assessment (QRA) is a powerful tool for the investigation and reduction of risk. It should be used to estimate the approximate probability of an accidental explosion during ammunition storage and then estimate the fatalities, injuries, damage and other losses from such an explosion (referred to as the consequences).
This enables professional judgement to be applied as to whether or not the risk meets the ALARP principal. It is used in the IATG software.
QRA provides an advantage over more subjective methods in that a more complete set of available information is used to quantify ‘risk’ as a parameter. This allows for consistency and repeatability from decision to decision, (for example when comparing the hazard presented by each explosive storehouse within an ammunition depot ).
The primary limitation of some of the techniques used within QRA (for explosives) is a degree of inherent uncertainty in the calculations. This is often due to the wide range of variables.
Nevertheless, accuracy in the absolute or overall sense can be discussed within ‘orders of magnitude’ (factors of 10) and still allow for appropriate decision-making.
Fidelity, that is the extent to which the QRA model is likely to be in comparison to a real life event, may be quite good.
Relative options can be compared with a degree of confidence.
<number>

## Slide 9: Risk Management Components
  Risk assessment
  Risk analysis
  Risk and ALARP evaluation.
  Hazard Identification
  Hazard Analysis
  Risk estimation
  Risk reduction
  Risk acceptance
  Risk communication
C7 Slide <number>
Notes: RISK MANAGEMENT COMPONENTS: (2 slides, 6 min)
SLIDE 1 of 2: RISK MANAGEMENT COMPONENTS (1 min)
To refresh your memories, the various components of risk management are:
Risk assessment
Risk analysis
Risk and ALARP evaluation.
Hazard Identification
Hazard Analysis
Risk estimation
Risk reduction
Risk acceptance
Risk communication
<number>

## Slide 10
Hazard Identification
Risk Estimation
Risk Analysis
Risk and ALARP evaluation
“Risk Assessment”
Risk Reduction
Risk Acceptance
Risk Communication
Risk Management
C7 Slide <number>
Notes: RISK MANAGEMENT COMPONENTS: (2 slides, 6 min)
SLIDE 2 of 2: DIAGRAM (5 min)
This is a somewhat confusing group of terms, so lets look at how the goal of ‘risk management’ is made up…
We start with hazard identification (sometimes called Hazard ID, or Haz ID).
We also estimate the risk posed by the hazards.
Together, these are ‘risk analysis’.
If we look at this risk analysis and try to determine if the risks are ‘as low as reasonably possible’ or ‘ALARP’ . So the risk assessment is the activity of looking at all of the hazards that we have identified and considering if they are indeed ALARP, and if not then by how much are they intolerable?
We then look at what extra risk mitigation measures could be put in place practicably, in order to reach an ALARP state.
Eventually we will get to the point where we know all of the risks are indeed ALARP. A this point, the head of establishment, or whoever else is responsible for bearing the risk, accepts the risk. This may, for example, be in a meeting for which the Minutes are formally recorded and filed to form an audit trail. The document detailing this risk process may also be personally signed by the person bearing the risk.
The risks and the mitigation measures then need to be communicated widely, and communication needs to be 2-way to ensure that these mitigation measures are physically put in place, and that stakeholders understand the risk both before and after mitigation.
This whole, complete process from initial theoretical hazard identification through risk assessment and acceptance and implementation of mitigation measures and a full communication process forms the top-level goal of ‘risk management’.
Tolerable risk is determined by the search for absolute safety contrasted against factors such as:
a) the inherent explosive safety hazards of storing, handling and processing ammunition;
b) available resources;
c) the conventions of the society where the ammunition is being stored; and
d) the financial costs.
This determination aides us in assessing whether risks are ALARP. The key factor here of course is 'practicable'.
<number>

## Slide 11: Risk Management Techniques
C7 Slide <number>
Notes: RISK MANAGEMENT TECHNIQUES: (7 slides, 13 min)
SLIDE 1 of 7: (no real time on this slide)
(Instructor: Header slide only, no time required on this slide. Move on to the next group of slides…)
<number>

## Slide 12: Hazard Identification and Analysis
Identify Explosive Storehouses (ESH)
Identify Potential Explosion Sites (PES)
  single ESH or
  clusters of close ESH
Identify what is to be stored in each ESH
Identify structure types and distances
C7 Slide <number>
Notes: RISK MANAGEMENT TECHNIQUES: (7 slides, 13 min)
SLIDE 2 of 7: HAZARD IDENTIFICATION AND ANALYSIS (2 min)
Hazard identification and analysis is a reasonably simple process for the risk management process that supports conventional ammunition storage.
As hazards are defined as a potential source of harm, then the hazard from, for example, individual explosive storehouses (ESH) will depend on
the quantity, hazard classification, physical condition and chemical stability of the ammunition contained within that ESH.
Normally each ESH is considered to be an individual Potential Explosion Site (PES).
However if there is a risk of practically instantaneous propagation due to inadequate distances between the ESH, then they may have to be treated as one single PES. In this case, the explosive quantities of each affected ESH may need to be aggregated to represent a single risk.
So the initial task is simply to determine what Potential Explosion Sites exist, and for each determine what is inside them. the distances between each type of ESH, and how they are constructed are also important, so a site plan will probably be necessary at this point.
<number>

## Slide 13: Risk Estimation
Risk = Probability x Consequence
Consequence analysis:
  The physical effects of such an explosion
  The number of casualties to be expected
  The levels of damage to be expected
C7 Slide <number>
Notes: RISK MANAGEMENT TECHNIQUES: (7 slides, 13 min)
SLIDE 3 of 7: RISK ESTIMATION (4 min)
As ‘risk’ is defined as a combination of the probability of occurrence of harm and the severity of that harm, then for explosive events in ammunition storage areas the estimation of risk should establish and/or estimate:
1. The 'consequence analysis' which includes:
a. The physical effects of such an explosion
b. The number of casualties to be expected
c. The levels of damage to be expected
Note that the IATG software includes an ‘automated’ Explosion Consequence Analysis, or "ECA" which just requires the input of basic readily
available data.
...and...
2. The probability of an unplanned and undesirable explosive event
To consider these further, but very briefly:
The physical effects of such an explosion: The physical effects of an undesirable explosive event within an ammunition depot can be estimated by using the appropriate equation contained within IATG 01.80 “Formulae for ammunition management”. This can be used to determine the blast over-pressure and impulse at the distance from a potential explosion site to an exposed site from a known explosive mass.
The number of casualties to be expected: For fatalities and injuries to humans, the threshold blast over-pressures have been established by experimentation. 34,5kPa is required for onset of hearing damage, 207kPa for lung damage and 690kPa for fatality. Therefore if the population density is known within the appropriate ranges, an estimate of the total number of fatalities and casualties can then be derived.
The levels of damage to be expected: As with damage to people, the effects of blast on buildings within and outside the perimeter of the ammunition depot
can be estimated. More on this topic is again covered in IATG 01.80 “Formulae for ammunition management”.
The probability of an unplanned and undesirable explosive event: Data on the number of annual ammunition depot accidents is available. A stockpile management organisation should be aware of previous similar events in their region; this will assist the organisation in assessing frequency, and hence probability. Alternatively, Logic or fault tree approaches are often used depending upon the complexity of and number of proposed scenarios
leading to an event.
<number>

## Slide 14: Risk and ALARP Evaluation
Compare:
  Estimated effects of human fatalities
  Estimated effects of human injuries
  Financial costs
  Political impact
Against what is tolerable in society
If tolerable and ALARP, further action may not be necessary
C7 Slide <number>
Notes: RISK MANAGEMENT TECHNIQUES: (7 slides, 13 min)
SLIDE 4 of 7: RISK AND ALARP EVALUATION (2 min)
The aim of risk evaluation is to compare the estimated effects, in terms of human fatalities and injuries, financial costs and political impact of an explosive event against what is tolerable in society.
If the risk is assessed as tolerable then no remedial action should be required, although it should also be considered if that risk is As Low as Reasonably Practicable (ALARP).
Some societies may consider a method of assessing the estimated 'individual risk of fatality' against other risks of fatality such as road traffic accident fatalities or from industrial processes, for example.
If the risk is not assessed as being tolerable then appropriate remedial action should be taken in order to reduce the risk.
<number>

## Slide 15: Risk Reduction
  Reduce stock levels in the area/building
  Increase separation distances
  Improve the physical infrastructure
  Surveillance and proof program for ammunition
  Close the depot and transfer stocks to another
  or…
  Formally accept the risk to the local community
C7 Slide <number>
Notes: RISK MANAGEMENT TECHNIQUES: (7 slides, 13 min)
SLIDE 5 of 7: RISK REDUCTION (2 min)
In order to reduce the estimated risk from an unplanned or undesirable explosive event at an ammunition storage area, one or a combination of the following actions can be taken:
A reduction of ammunition stock levels within the explosive storage area until appropriate predicted blast over-pressure levels are reached at the exposed site (This is a LEVEL 1 activity in the risk reduction hierarchy).
An increase in the separation distance between the potential explosion site and the exposed site until tolerable blast over-pressure levels are reached at the exposed site (LEVEL 2).
Improvements in the physical infrastructure of ammunition storage to achieve tolerable estimated blast over-pressure levels at the exposed site (LEVEL 2 and 3).
Instigation of effective ammunition surveillance and proof systems to identify ammunition and propellant that has deteriorated to a dangerous condition (see IATG 07.20 Surveillance and proof) (LEVEL 3).
Closure of the ammunition depot and the transfer of stocks to an ammunition depot with spare capacity (LEVEL 1).
The probable impact of the estimated risk to the local community is formally accepted at the appropriate political level (LEVEL 1).
<number>

## Slide 16: Risk Communication
C7 Slide <number>
Notes: RISK MANAGEMENT TECHNIQUES: (7 slides, 13 min)
SLIDE 6 of 7: RISK COMMUNICATION (1 min)
The risk managers should identify people, organisations and even pressure groups who have some form of interest in the risk and activities at the site, and classify these as ‘stakeholders’.
Risk communication is the process of exchange of information and opinion on risk, and this works both ways.
Risk communication is an integral and ongoing part of the risk management process, and ideally all stakeholder groups should be involved from the start. Risk communication makes stakeholders aware of the results of the risk assessment, the logic behind the risk analysis process, and the remedial measures taken to ensure a level of tolerable risk.
<number>

## Slide 17: Risk Acceptance
Risk Acceptance Criteria:
  Perceptions of societal risk
  Costs
  Environmental impact
Accept the risk formally:
  Sign off an appropriate explosive license
  If risk is intolerable, formally accept the residual risk
  If required: escalate the matter up government levels
C7 Slide <number>
Notes: RISK MANAGEMENT TECHNIQUES: (7 slides, 13 min)
SLIDE 7 of 7: RISK ACCEPTANCE (2 min)
Risk acceptance criteria will result from three factors:
Local perceptions of societal risk and hence the detailed specification of ‘tolerable risk’
The potential economical cost and losses due to an undesired explosive event (which will include):
  Explosive ordnance disposal remediation costs
  Reconstruction costs (for public and civilian buildings)
  Injury compensation costs
  Ammunition replacement costs)
A supporting Cost Benefit Analysis (CBA) may be required before the risk may be formally accepted as it could impact on tolerable risk and hence require a reiteration of the risk assessment process
3. Environmental impact
To conclude:
Where tolerable risk has been achieved, and if necessary supported by CBA, then that risk and the residual risk should be formally accepted by the appropriate authority within a conventional ammunition stockpile management organisation. In terms of ammunition storage this should usually take the form of issuing Explosive Licences for the ammunition storage area.
Where tolerable risk has not been achieved, and where resources are not being made available to achieve tolerable risk in the short term, then the residual risk should be formally accepted in writing by the entity responsible for the allocation of resources to the stockpile management organisation
Should the resource allocation entity refuse to formally accept the risk in writing, then the issue should be referred to the next level of government for reconciliation of the issue.
<number>

## Slide 18: Questions
C7 Slide <number>
Notes: Are there any questions? 1 slide, 5 minutes
<number>