## Slide 1: Bans and Constraints
C6 Slide <number>
Notes: INTRODUCTION:
SLIDE 1 of 1: INTRODUCTION (1 min)
Bans and constraints on the use, storage, handling, transportation or disposal of conventional ammunition are a fundamental component of a safe, effective and efficient ammunition management system.
They are primarily issued by the conventional ammunition stockpile management organisation to control the issue and use of explosives and ammunition to make sure that the users receive ammunition that is:
Safe to use
Will perform within the agreed ballistic and performance envelopes.
Constraints on the use of ammunition may also be used to protect ammunition stock levels during shortages of certain types of ammunition.
It is essential for the safety and morale of users that they receive ammunition that they have confidence in; a system of ammunition bans and constraints, instigated by the conventional ammunition stockpile management organisation, ensures this.
<number>

## Slide 2: Definition - Ban?
A ban on the use of specific conventional ammunition, (which may be at generic type, lot, batch and/or serial number level), should be imposed to prevent the issue or use of conventional ammunition.
C6 Slide <number>
Notes: DEFINITIONS: (3 SLIDES, 5 MIN)
SLIDE 1 of 3: DEFINITION - BAN (2 min 30 sec)
A ban on the use of specific conventional ammunition, (which may be at generic type, lot, batch and/or serial number level), should be imposed to prevent the issue or use of conventional ammunition. In essence, ammunition which is subject to a Ban must not be issued or used at all.
<number>

## Slide 3: Definition - Constraint?
Constraints are the imposition of a limitation or restriction in the use, transportation, carriage, issue, storage or inspection of munitions.
Constraints should be used as a tool for the ammunition management system.
C6 Slide <number>
Notes: DEFINITIONS: (3 SLIDES, 5 MIN)
SLIDE 2 of 3: DEFINITION - CONSTRAINT (2 min 30 sec)
Constraints, (which may be at generic type, lot, batch and/or serial number level), are the imposition of a limitation or restriction in the use, transportation, carriage, issue, storage or inspection of munitions.
<number>

## Slide 4: Ban v Constraint
BAN:
OUTRIGHT
CONSTRAINT:
ALLOWS SOME FLEXIBILITY
C6 Slide <number>
Notes: DEFINITIONS: (3 SLIDES, 5 MIN)
SLIDE 3 of 3: BAN v CONSTRAINT – THE DIFFERENCE (2 min)
A Ban means a total block on issue and use of the affected ammunition. Full stop.
A constraint allows some use, but prohibits other uses. This offers some flexibility for managing stocks that may have limitations without having to make that whole stock of that particular ammunition redundant.
Constraints normally remain in force for the life of ammunition, while a ban can be a short-term measure. That said, a constraint may be short-term if there is a low stock level and this needs managing until more supplies are received. Alternatively, a ban be long term if, for example, a technical investigation is ongoing but this is difficult and protracted.
<number>

## Slide 5: Rationale - Bans
Bans might be applied:
  If the nature is suspected of being the cause of an ammunition accident
  When there have been excessive performance failures
  When a defect, which could compromise safety, has been discovered
  When the ammunition is to be withdrawn at the end of its serviceable life
C6 Slide <number>
Notes: RATIONALE: (2 SLIDES, 5 MIN)
SLIDE 1 of 2: RATIONALE - BANS (2 min 30 sec)
The rationale for using bans – as in an outright ban – is to avoid use when there may be safety hazards and risks associated with that particular ammunition type. Often, bans are used when there is uncertainty about the conditions under which an ammunition nature might malfunction. Bans can also be applied for similar reasons relating to reliability.
Examples of situations when a ban might be applied are:
When it is suspected of being the cause of an ammunition accident, irrespective of whether death or injury has been caused
When there have been excessive performance failures
When a defect, which could compromise safety, has been discovered
When the ammunition is to be withdrawn at the end of its serviceable life
In ideal circumstances, an investigation will identify the failure mode through which the hazard occurs. In this case, it may be possible to lift the ban if the risk can be managed and is tolerable.
<number>

## Slide 6: Rationale - Constraints
Constraints may be applied to the use, storage, handling, transportation or disposal of ammunition. Examples:
  Storage temperatures to be adhered to
  Special handling requirements
  A decision that ammunition is for training use only
  A change of shelf life parameters
C6 Slide <number>
Notes: RATIONALE: (2 SLIDES, 5 MIN)
SLIDE 2 of 2: RATIONALE – CONSTRAINTS (2 min 30 sec)
There may be knowledge about how a safety hazard (or reliability failure) manifests itself. This may allow use of the affected ammunition within managed limitations, such that the situation which causes the failure mode should not be encountered.
This is different from the kind of situation when a ban may be deemed necessary if there is no or insufficient knowledge about how the failure mode comes about.
Constraints may be applied to the use, storage, handling, transportation or disposal of ammunition.
An example could be, say, a particular batch of 7.62mm machine gun ammunition which experienced a number of hangfires when used in one type of machine gun at maximum depression. Investigation identified that this fault would not occur in other types of machine gun in the inventory. The risk therefore only seems to apply to one weapon system. The Constraint might therefore state that this particular batch is not to be issued for use, and used in, this weapons system that seems to be affected. This does however mean that the stock is still acceptable for issue and use in the unaffected weapon systems.
In essence, constraints should be used as a tool to run the ammunition management system more efficiently and effectively.
Other examples of constraints include:
Storage temperatures to be adhered to
Special handling requirements
A decision that ammunition is for training use only
A change of shelf life parameters
<number>

## Slide 7: Content and Dissemination of a Ban and Constraint
The type and calibre of ammunition
The specific lot, batch and/or serial number of the ammunition to which the ban or constraint applies
Full details of the ban or constraint, which may require:
  A total cessation of use
  A limitation which is necessary during use, storage, handling, transportation or disposal
  A limitation in use during training
C6 Slide <number>
Notes: ACTIONS BY USER UNITS: (3 SLIDES, 9 MIN)
SLIDE 1 of 3: CONTENT AND DISSEMINATION OF A BAN AND CONSTRAINT (3 min)
Any ban or constraint on the use of specific or generic ammunition should contain the following information, which shall be disseminated to users as soon as possible:
a) the type and calibre of ammunition
b) the specific lot, batch and/or serial number of the ammunition to which the ban or constraint applies
c) full details of the ban or constraint, which may require:
i) a total cessation of use
ii) a limitation which is necessary during use, storage, handling, transportation or disposal
iii) a limitation in use during training
Dissemination of bans and constraints:
The organisation responsible for the overall conventional ammunition management system should ensure that an appropriate system is in place that can rapidly alert users to the imposition of an ammunition ban and constraint. Details of the ban or constraint should reach the user units through this system, in a timely manner.
<number>

## Slide 8: Action on Notification of a Ban
Mark the ammunition packaging or container:
i) ‘NOT FOR ISSUE OR USE’
ii) the ban serial number
iii) any special instructions received with the ban
Enter details ban in the ammunition account
Arrange for the ammunition to be transported to the designated ammunition demilitarization or destruction organisation as required
C6 Slide <number>
Notes: ACTIONS BY USER UNITS: (3 SLIDES, 9 MIN)
SLIDE 2 of 3: ACTION ON NOTIFICATION OF A BAN (3 min)
Users should take the following action when they receive notice of an ammunition ban from the conventionna ammunition stockpile management organisation:
a) mark the ammunition packaging or container with the following information:
i) ‘NOT FOR ISSUE OR USE’
ii) the ban serial number
iii) any special instructions received with the ban
b) enter the details of the ban in the user’s ammunition account
c) arrange for the ammunition to be transported to the designated ammunition demilitarization or destruction organisation as required.
<number>

## Slide 9: Action on Notification of a Constraint
Mark the ammunition packaging or container:
i) the constraint serial number
ii) details of the constraint
Enter the details of the constraint in the user’s ammunition account
C6 Slide <number>
Notes: ACTIONS BY USER UNITS: (3 SLIDES, 9 MIN)
SLIDE 3 of 3: ACTION ON NOTIFICATION OF A CONSTRAINT (3 min)
Users should take the following action when they receive notice of a constraint on ammunition use, storage, handling, transportation or disposal from the conventional ammunition stockpile management organisation:
mark the ammunition packaging or container with the following information:
i) the constraint serial number
ii) details of the constraint
b) enter the details of the constraint in the user’s ammunition account.
<number>

## Slide 10: Mini Exercise: Bans and Constraints
C6 Slide <number>
Notes: MINI EXERCISE: (2 SLIDES, 20 MINUTES)
SLIDE 1 of 2: MINI EXERCISE: BANS AND CONSTRAINTS
(Instructor):
Get the students to look at their hand-out sheet. They should take 5 minutes to read through this and assimilate the information.
Get the students to take 5 minutes to answer the three questions on the back of the sheet. There are prompts for them here.
At the 10 minute point, stop the students.
Lead a discussion group for 5 minutes on their ideas and thoughts.
The recommended solution at this point is to apply a ban, but only on 7.62mm 4B/1T, RG 03-11 Lot 003. This is in recognition of the fact that there is an abnormally high misfire rate. The cause is not known. This is a training exercise only. Furthermore, there is a technical investigator deploying to the scene who should be able to assess the problem. This will provide further information for the Investigating Authority, who may be able to lift the ban and manage the issue with a constraint, perhaps in the near future. The unit has sufficient stock of another seemingly fine Lot with which to complete the exercise.
In the final 5 minutes of the mini-exercise session, test their wider appreciation of these matters. This development is not on their data/question sheets. Tell them that 10 minutes after the ban was promulgated, the staff officer received a phone call from the Officer Commanding the Infantry Battalion deployed on border security on the country’s northern border. 50% of his stock of 7.62mm ammunition is made up of Lot 003. He wants to know why he can’t use it as this means he will have insufficient ammunition to meet his deployment liabilities for sentries. He could potentially rotate the other Lots of ammunition from his ammunition store out to the check points but this would take significant effort and several days. Ask the students to consider this and lead discussion. Try to see if there is a majority, or not, either way. Examples may include insisting the OC rotates his stock and keeping the ban, changing the ban to constraint that only permits operation use only, and so on.
This mini-exercise should take 20 minutes in total.
<number>

## Slide 11: Questions
C6 Slide <number>
Notes: Are there any questions? 1 slide, 5 minutes
<number>