## Slide 1: Ammunition Accidents
C12 Slide <number>
Notes: INTRODUCTION: (1 slides, 1 minute)
SLIDE 1 of 1: BACKGROUND (1 min)
The reporting and investigation of conventional ammunition accidents is a key component in the safety management of conventional ammunition stockpiles during storage, handling and use
Accidents or incidents involving conventional ammunition are a regular occurrence, even in the best-trained military and security forces, even though most of them are preventable.
Reporting and investigating accidents will establish lessons for others to learn and ultimately contribute to improved safety for all.
<number>

## Slide 2: Types of Accident
Accident: Is an incident resulting in death/injury to a person(s) and/or damage to assets.
C12 Slide <number>
Notes: TYPES OF ACCIDENT: (1 slide, 3 minutes)
SLIDE 1 of 1: TYPES OF ACCIDENT (3 min)
By way of explanation:
An ammunition accident, irrespective of cause or however minor, is any incident involving ammunition and explosives that results in death or injury to a person(s) and/or damage to equipment and/or property, military or civilian.
3 illustrative examples of accidents are:
A breech explosion occurs in a weapon, injures the firer and causes damage to the working parts.
A battle simulation charge explodes in close proximity to a soldier causing flash burns and temporary deafness.
A ricochet of a small arms bullet hits and damages a vehicle parked on the range.
<number>

## Slide 3: Rationale for Reporting
To inform system managers of problems…
To allow the system manager to investigate…
To identify safety risks or reliability problems…
To implement mitigation measures…
To reduce the risk of repeat events.
C12 Slide <number>
Notes: RATIONALE FOR REPORTING: (2 slides, 10 minute)
SLIDE 1 of 2: THE REASON FOR REPORTING (7 min)
Why is a ‘reporting and investigation’ approach so important? An unplanned event may occur because there is some shortfall in any number of factors that come together to make the equipment reliable and safe. This shortfall may not have been identified my the manager of the system. If the problem has happened once, it may happen again. By reporting the problem, and then conducting an investigation into the cause of the problem, the manager of that system might identify a potential problem that could keep happening. This repeating, or systematic fault, might be undesirable, especially if it would render a number of operationally important systems as unserviceable, or if there was a safety concern like an operator was killed every time the event occurs. By identifying the problem, and its likely consequences, the manager will be able to consider suitable mitigation measures.
So the investigation process is primarily to find and solve safety problems and reliability problems. This is in everyone’s interests.
But problems can only be identified and looked into if the manager knows there is a problem in the first place. So it is imperative that the user units report all problems. And they must report them immediately, to allow timely consideration by the system manager.
Furthermore, it is necessary to report all problems.
It is not the users’ prerogative to decide whether something is ‘too small to be worth bothering with’. This is because there may be thousands of these ‘small problems’ – which cumulatively pose a risk is unacceptable because it happens so often.
Alternatively, a ‘small’ event may be a ‘near miss’ – the operator may have been lucky that nothing worse occurred. However the same fault, if it occurs again, might produce far wore results and injure the operator, degrade an operational capability, and so on.
As a worked example:
A rifleman is training on military range. He is using a practice hand grenade. He posts the grenade into a shallow ditch, in accordance with drills. He is supervised by a qualified and experienced training officer. The training grenade produces a much louder noises than expected, and is projected straight back at the rifleman. It strikes the safety officer in the face, blinding him. The safety officer is unable to continue serving and is discharged on medical grounds. The training officer was the only expert in the force on a newly procured guided weapon system. The medical discharge costs the government in cost of medical treatment, casualty evacuation by helicopter, pension costs. The expertise on the new weapon system is also lost. It becomes apparent that this same type of event has happened at least 10 times in the previous 6 months, but it wasn’t reported as no one was hurt but the training units couldn’t be bothered to report the incidents. The investigation identifies that the practice grenade may responds in this way if dropped base first into soft, waterlogged mud. Had the system manager known, he could have taken temporary measures to restrict use of the training grenade while he investigated the cause. The cause would have been identified, potentially with relative ease, and advice offered to units to the effect that they should check where a training grenade is to be posted beforehand, specially if the ground is soft and wet. In this case, the rifleman wouldn’t have dropped the grenade in that type of land, and so the event would not have occurred. The force would have avoided the medical and related costs and effort, and retained expertise in the new missile system.
<number>

## Slide 4: Safety Culture
Reporting Culture
Just Culture
Flexible Culture
Learning Culture
Questioning Culture
C12 Slide <number>
Notes: RATIONALE FOR REPORTING: (2 slides, 10 minutes)
SLIDE 2 of 2: SAFETY CULTURE (3 min)
A reporting system that works relies on troops reporting incidents in the first place, and reporting them correctly, honestly and completely.
In environments where fault is seen as a punishable offence, for example, it must be considered unlikely that troops will report in that way, if at all.
As an example, if soldiers routinely get beaten or humiliated through rituals, they will not report incidents. They will attempt to hide the evidence and potentially lie about things that have occurred.
As such, there needs to be a sound environment – a culture – within the organisation that treats people fairly, even if they have made mistakes. There needs to be a fair, honest reporting culture. Indeed, this is all part of a higher level safety culture which again must be seen as desirable and is worth pursuing.
A safety culture may be seen as being based on 5 key elements:
Reporting Culture
Just Culture
Flexible Culture
Learning Culture
Questioning Culture
This may be a big cultural leap for some entities, however development of a safety culture should certainly aide a safer and more responsible environment. This 5-element model comes from the Haddon-Cave Nimrod Report for the UK MOD, 2009.
<number>

## Slide 5: Action by User Units
Cease firing
First aid to any injured personnel / cover bodies and summon medical assistance
Cordon off the area, leave everything 'in-situ'
Take names of potential witnesses
Weapon involved 'made safe' (as necessary) and secured
Immediately report the ammunition accident
C12 Slide <number>
Notes: ACTION BY USER UNITS: (2 slides, 10 minutes)
SLIDE 1 of 2: ACTION BY USER UNITS (5 min)
The unit using the ammunition should take the following actions in the event of an ammunition accident:
Cease firing.
Give immediate first aid to any injured personnel. In the case of fatal accidents, bodies should not be touched except to confirm death. Out of respect, bodies should be covered until they can be removed from the scene.
Summon medical assistance if required.
Cordon off the area to preserve evidence for the investigating authority. Nothing should be moved and everything should remain as it is in situ.
Record the names of potential witnesses.
Make safe the individual weapon involved and secure it for the investigating authority. The weapon should only be touched if there is a requirement to make it safe to prevent further injuries.
Immediately report the ammunition accident in accordance with the relevant, extant instructions (probably by completing an Accident Form) and wait for further guidance from the nominated technical investigator.
Firing may recommence before the arrival of the investigating authority providing there have been no injuries, a different lot, batch or type of ammunition or explosive is used and the scene of the incident remains undisturbed.
The reason for leaving everything ‘as is’, commensurate with safety, is to allow the investigation officer the opportunity to see the situation ‘as is’.
Many investigations have been needlessly hampered because a local commander has decided to pack everything up and move on to some other training serial, or whatever.
<number>

## Slide 6: Ammunition Incident Reporting Form
C12 Slide <number>
Notes: ACTION BY USER UNITS: (2 slides, 10 minutes)
SLIDE 2 of 2: AMMUNITION INCIDENT REPORTING FORM (5 min)
The national authority or the organisation responsible for the stockpile management of conventional ammunition should ensure that a system of reporting and investigating ammunition accidents is developed, promulgated to all users and is then effectively used.
Users should be instructed to immediately report the information on an ammunition accident to the appropriate investigating authority.
The reporting form is likely to include the following information. A template reporting form is on the screen - this is taken from IATG 11:10, Annex C.
Name of individual reporting fault or performance failure
User unit
User unit contact person
Date and time of ammunition accident
Details of any fatalities and/or injuries
Location where the ammunition accident has occurred, including map grid reference
Type of ammunition involved (full technical name)
Weapon type involved (full technical name)
Batch, lot and/or serial number of the ammunition involved
Brief description of accident
Weather conditions
Action taken by user unit
<number>

## Slide 7: Investigation Authority Requirements
Investigation Authority
Appointed by the ammunition stockpile management organisation
Maintain a pool of competent, experienced personnel
Devise and promulgate a Reporting Form
Appoint a technical investigator for each incident
C12 Slide <number>
Notes: INVESTIGATION AUTHORITY REQUIREMENTS: (4 slides, 15 minutes)
SLIDE 1 of 6: INVESTIGATION AUTHORITY REQUIREMENTS (3 min)
The conventional ammunition stockpile management organisation needs to establish an Investigating Authority. This Investigating Authority needs to maintain a team of suitably competent and experienced individuals as technical investigators available to undertake an initial investigation in the event of an accident. These individuals should have a sound understanding of the extant explosive and other safety regulations and of local procedures applicable to the area in which the accident has occurred. They should also have appropriate technical expertise.
The Investigating Authority needs to have devised and promulgated a Reporting Form which users are aware of and are able to complete.
For each ammunition incident that is reported, an independent technical investigator needs to be appointed. The Technical Investigator shall not have been involved with the accident in any way.
<number>

## Slide 8: The Technical Investigator
Examine the scene of the ammunition accident
Examine any weapon involved
Visually inspect any pieces of the ammunition involved
Recover pieces of ammunition/destroy if unsafe to move
Examine other ammunition of the same type/lot/batch
Question any appropriate witnesses
Make an initial technical appraisal of the cause
C12 Slide <number>
Notes: INVESTIGATION AUTHORITY REQUIREMENTS: (4 slides, 15 minutes)
SLIDE 2 of 6: THE TECHNICAL INVESTIGATOR (5 min)
The technical investigator will:
Examine the scene of the ammunition accident
Examine any weapon involved, possibly with a weapon armourer
Visually inspect any pieces of the ammunition involved
Recover any pieces of the ammunition that was involved for further technical investigation or destroy, after consultation with the appropriate technical authority, if unsafe to move
Examine other ammunition of the same type, and lot, batch or serial number being used at the same time
Question any appropriate witnesses
Make an initial technical appraisal of the cause of the ammunition accident and recommend any appropriate bans or constraints to the investigating authority
If appropriate, impose an immediate local ban on the use of the ammunition (by lot, batch or serial number) involved in the ammunition accident
Submit a written ammunition accident report to the investigating authority in the appropriate format.
It is not the job of the Technical Investigator to attribute blame or negligence to any individual.
<number>

## Slide 9: The Technical Investigator
Recommend appropriate bans or constraints
If appropriate, impose an immediate local ban
Submit a written ammunition accident report
C12 Slide <number>
Notes: INVESTIGATION AUTHORITY REQUIREMENTS: (4 slides, 15 minutes)
SLIDE 3 of 6: THE TECHNICAL INVESTIGATOR (5 min)
The technical investigator will:
Examine the scene of the ammunition accident
Examine any weapon involved, possibly with a weapon armourer
Visually inspect any pieces of the ammunition involved
Recover any pieces of the ammunition that was involved for further technical investigation or destroy, after consultation with the appropriate technical authority, if unsafe to move
Examine other ammunition of the same type, and lot, batch or serial number being used at the same time
Question any appropriate witnesses
Make an initial technical appraisal of the cause of the ammunition accident and recommend any appropriate bans or constraints to the investigating authority
If appropriate, impose an immediate local ban on the use of the ammunition (by lot, batch or serial number) involved in the ammunition accident
Submit a written ammunition accident report to the investigating authority in the appropriate format.
It is not the job of the Technical Investigator to attribute blame or negligence to any individual.
<number>

## Slide 10: Investigation Authority Actions
Examine the technical investigators’ reports
Classify the accident
Consult with other appropriate organisations
Make a technical judgement as to the cause
Initiate remedial action to prevent a reoccurrence
Inform the user unit of the results of the investigation
C12 Slide <number>
Notes: INVESTIGATION AUTHORITY REQUIREMENTS: (4 slides, 15 minutes)
SLIDE 4 of 6: THE INVESTIGATION AUTHORITY ACTIONS (3 min)
The Investigation authority, upon receiving the technical investigator’s report, will conduct the following activities:
Examine the reports submitted by technical investigators on ammunition accidents
Classify the accident (which we will look at next)
Consult with other appropriate organisations (manufacturers, designers, procurement agencies etc) to obtain further information as necessary
Make a technical judgement as to the cause of the ammunition accident, although this may take place under the auspices of a national legal framework (i.e. a Board of Inquiry) depending on the extant national legal requirements (possibly using the suggested ‘closure codes’ provided in IATG 11:10)
Initiate remedial action to prevent a reoccurrence
Inform the user unit of the results of the investigation
Maintain records of all ammunition accidents
Provide technical advice to the conventional ammunition stockpile management organisation as appropriate
<number>

## Slide 11: Investigation Authority Actions
Maintain records of all ammunition accidents
Provide technical advice to the conventional ammunition stockpile management organisation
C12 Slide <number>
Notes: INVESTIGATION AUTHORITY REQUIREMENTS: (4 slides, 15 minutes)
SLIDE 5 of 6: THE INVESTIGATION AUTHORITY ACTIONS (3 min)
The Investigation authority, upon receiving the technical investigator’s report, will conduct the following activities:
Examine the reports submitted by technical investigators on ammunition accidents
Classify the accident (which we will look at next)
Consult with other appropriate organisations (manufacturers, designers, procurement agencies etc) to obtain further information as necessary
Make a technical judgement as to the cause of the ammunition accident, although this may take place under the auspices of a national legal framework (i.e. a Board of Inquiry) depending on the extant national legal requirements (possibly using the suggested ‘closure codes’ provided in IATG 11:10)
Initiate remedial action to prevent a reoccurrence
Inform the user unit of the results of the investigation
Maintain records of all ammunition accidents
Provide technical advice to the conventional ammunition stockpile management organisation as appropriate
<number>

## Slide 12: Classification of Accidents
Fatal
Major
Serious
Minor
Near Miss
Negligent Discharge
FFE Violation
C12 Slide <number>
Notes: INVESTIGATION AUTHORITY REQUIREMENTS: (4 slides, 15 minutes)
SLIDE 6 of 6: CLASSIFICATION OF ACCIDENTS (4 min)
The following classification system is provided in IATG 11:10:
Fatal (personnel)/Critical (equipment): An occurrence involving ammunition which causes one or more of the following:
A fatality or severe injuries resulting in long term illness or disability to military personnel or members of the public.
Extensive loss, damage to, or contamination of military or civilian equipment or property at multiple facilities, or to the environment.
Major: An occurrence involving an ammunition which causes one or more of the following:
Severe injuries resulting in hospital treatment to military personnel or members of the public.
Loss, damage to, or contamination of the munition or explosive, or to military or civilian equipment or property at a single facility.
Serious: An occurrence involving ammunition which causes one or more of the following:
Injury requiring medical treatment and time off work but which does not require hospital treatment.
Minor loss, damage to the munition or explosive or minor contamination of, military or civilian equipment, property, or the environment.
Minor: An occurrence involving ammunition which causes one or more of the following:
An injury or illness to military personnel or members of the public.
Cosmetic damage to ammunition not affecting performance or safety.
Near Miss: An occurrence, or potential occurrence, involving ammunition, or an occurrence potentially involving ammunition, which could have caused:
Damage to the ammunition.
Damage to, or contamination of, military or civilian equipment, property or the environment.
Injury to, or illness of, military personnel or members of the public.
Threat to the structural integrity of, or to cause damage to, military or civilian equipment, property or the environment.
Free From Explosives (FFE) Violation.
Negligent Discharge: A discharge of small arms ammunition (SAA) up to and including 14.5mm calibre from a weapon as a result of preventable human failing, where no injury or damage has occurred and the weapon and munition performed to the designed specification.
Free From Explosive (FFE) Violation: The discovery of ammunition item(s) within containers that have been certified FFE.
<number>

## Slide 13: Questions?
C12 Slide <number>
Notes: Are there any questions? (allow 5 minutes for questions)
If there are no questions, test their understanding about the need for reporting and how it relates to safety management, what the unit might be expected to do as the immediate response to an incident, and suggest what might be expected of the technical investigator.
<number>