## Slide 1: Quantity Distance Exercise
45 minute Test Exercise
MA05 Slide <number>
Notes: INTRODUCTION: (3 SLIDES, 10 MIN)
SLIDE 1 of 3: INTRODUCTION (1 min)
You will now do an exercise which will practice you in the calculation and application of Quantity Distances.
This session will take 45 minutes.
I will take 5 minutes to brief you and to provide some background.
You will then have 5 minutes to read over the information and gain an understanding of the scenario.
You will then take 10 minutes to do the first part of the exercise, which is calculating the QD for ESH number 4 in relation to HD 1.1
We will then take 5 minutes to review the answers and draw some conclusions.
You will then have 10 minutes to do the second part of the exercise, which is to calculate the QDs for all HDs, for ESH number 1.
We will then take 10 minutes to review the answers and to discuss any points arising, including questions that you may have.
You will need to use the handouts, including the QD tables and the ELL Matrix.
You will be doing these calculations manually. That means that you will not use any computer programs. You may of course use your calculators and your fingers and thumbs to do the necessary sums.
You may use scrap paper to do your working out if you so wish.
<number>

## Slide 2: Background
MA05 Slide <number>
Notes: INTRODUCTION: (3 SLIDES, 10 MIN)
SLIDE 2 of 3: BACKGROUND (3 min)
You are the nominated officer responsible for the ammunition storage on a UN deployment to foreign country. This deployment is a peace-keeping operation to provide a permissive environment for political reform. The country has had a recent history of armed violence from criminal elements and also a rebel faction in the north of the country. There is estimated to be a high quantity of small arms and light weapons in the hands of the civilian population due to illegal smuggling from the neighbouring country. There are not thought to be any armoured vehicles in rebel hands.
The indigenous armed forces are of average capability, they are essentially a lightly mechanised infantry force with some supporting elements. They are useful for security activities.
The military infrastructure and organisation is based on a generic European model. This includes the legacy of several ammunition depots which are located across the country. These were built to a high standard approximately 50 years ago.
You have been offered one of these explosive facilities by the national government. It is empty so you are free to use it as you wish. The facility is close to the coast in a remote, rural area surrounded by forest. The fabric of the buildings, roads and related infrastructure is actually quite good. There are omissions like a distinct lack of fire extinguishers and hazard signs, however you will look at fixing this problem once you have decided which ammunition buildings to use. You will also need to do some cleaning and preparation to get the site ready.
The UN force is deploying with armoured personnel carriers and light support vehicles (trucks and jeeps). This means a number of 7.62mm machine guns (1 per vehicle for protection).
The troops are equipped with 5.56mm and 7.62mm assault rifles, plus 9mm pistols as a personal protection weapon in case their rifle fails. The each also carry a few HE anti-personnel grenades.
In addition, there are a number of ammunition natures for use by the troops for protection and signalling. These include smoke grenades, handheld mini-flares for signalling, handheld parachute illumination flares, and tripflares.
The last type of ammunition to mention is demolition charges for the Explosive Ordnance Disposal Teams. There is a significant UXO problem in the country.
The details of this ammunition stock on the manifest are in your exercise handout.
The ammunition will be delivered direct to the depot by truck. The truck convoys will come with its own forklift truck. It will be packed onto standard 1 tonne pallets.
Each pallet is to be classed as one Unit of Space.
There is no forklift truck which is dedicated to the depot. You can only be guaranteed hand palletisers/pallet trucks. You may therefore only place the pallets as one single layer. You may not stack pallets on top of each other.
The Force Commander has ordered you that, if at all possible, each type of ammunition should be divided into two – ie split across two separate storage sites within the explosive facility, to offer some degree of protection from accident, sabotage or even enemy action. The exception to this is the EOD stores which should all go into one ESH, if possible, at the request of the EOD teams.
There is no dedicated demolition ground, however the EOD team commander has said he should be able to dispose of stores for you safely, so you should try to keep him ‘on side’.
For the reasons of protection and security, you are only to use the available ESH. You are not to use stacks in the open (eg on hard standing).
Your task for this exercise, therefore, is to start calculating the options for ammunition storage, and then identify a workable allocation of ammunition stocks to the available sites.
The Force Commander has ordered that you must abide by the requirements of the IATG document set, particularly regarding the Quantity Distances in IATG 02:20.
<number>

## Slide 3: Tips
Units of Space per ammunition type
Split stocks in two for protection
NEQ per Unit of Space
Only 1 layer of pallets – no stacking
Consider how many Units of Space there at which ESH
Identify the correct pictograms (igloo headwalls/doors!)
Calculate QD for each HD for each ESH (correct tables!)
Use the ELL Matrix to record findings
Consider mixing rules and aggregation to mix HCCs
Allocate stock to ESH
MA05 Slide <number>
Notes: INTRODUCTION: (3 SLIDES, 10 MIN)
SLIDE 3 of 3: TIPS (6 min)
(Instructor: very quickly list these points in 1 minute, do not go into detail).
Here are a few tips to get you started:
Identify how many Units of Space for each type of ammunition are required.
Divide these figures in two as the stocks need to split for protection.
Identify the NEQ per Unit of Space for each ammunition type.
Only 1 layer of pallets – no stacking.
Consider how many Units of Space there at which ESH.
Identify the correct Pictogram, especially for the earth-covered igloo based on the type of headwall and doors. The wording in the text is as per the tables).
Calculate the permissible QD for each HD, for each ESH as required.
Make sure you use the right tables for each HD.
Use the ELL Matrix for this purpose to record your findings.
Consider mixing rules can you mix HCCs.
Allocate stock to ESH.
Also, note that you also need to consider the truck marshalling/loading area as an explosive site (an open stack).
(Instructor: You should also check that they have picked up the subtle difference between a light structure, and a shed made of basic cladding which is effectively an open stack. Point out that the shaded box pictogram is a light structure, whereas an open stack/shed is the un-shaded box. They may also find it useful to add a column to the template table –for the site office/guardroom).
(Instructor: Tell the students to take 5 minutes to review the scenario and the associated Annexes).
(Instructor: After the students have had 4 to 5 minutes to review the scenario, click the slide to start Part 1 of the exercise).
<number>

## Slide 4: Part 1
Safety Culture
Options for storing HD 1.1 Demolition stores
To satisfy your curiosity, you first decide to check the possibility of using ESH 4
Calculate QDs for ESH 4 – HD 1.1 only!
10 minutes for this work
MA05 Slide <number>
Notes: EXERCISE: (1 SLIDES, 15 MIN)
SLIDE 1 of 1: PART 1 (15 min)
(Instructor: Pose these questions students verbally, and get them to reply verbally with their thoughts. This should only take a minute or two. This is to set the scene and to prime the students to think about the exercise, and also to get them to think about the overall ‘safety culture’ rather than just launching them into a ‘tick box exercise’.
Q1. Which ammunition natures do you think pose the highest explosive risk? (Answer: Probably the HD 1.1 demolition stores).
Q2. Which ESH do you think provides the most protection for such stores? (Answer: Probably the igloo, ESH 1).
Q3. Which type of ESH might be second best for storing HD 1.1? (Answer: Probably the reinforced heavy structures. Particularly the ESH 4, as although this hasn’t got a barricaded door, the angle of orientation of the building suggests there are no significant threats from an other sites).
Q4. Which ESH seems most secure from a security perspective? Why might this be relevant to the 1.1 demolition stores? (Answer: The igloo, ESH 1, has an intruder alarm and CCTV system, so this may well be most secure, although it is at the farthest end of the camp. Security would be important for this kind of store as they would be attractive to criminals and rebel forces who may be able to use them to make Improvised Explosive Devices, for example).
(Instructor: After a minute or two doing these verbal questions, commence the activity below):
To satisfy their (notional) curiosity they decide to check the scope for using ESH 4 for HD 1.1 demolition stores, which as we know are to be stored in a single ESH is possible at the request of the EOD team.
Launch the students on the Part 1 calculations.
They have 10 minutes to calculate the Quantity Distances for ESH 4, ONLY for Hazard Division 1.1.
They will probably find it easiest to use a blank template ELL Matrix from their handouts.
(Instructor: At the end of the 10 minutes, take a few minutes (but no more than 5 minutes) to review their answers with them. The key factor is: Because of the proximity to the site office (which is under 270m away), this ESH cannot be used for Hazard Division 1.1, as the separation distance is to low so the required Quantity Distance cannot be met).
<number>

## Slide 5: Part 2
ESH 1 (earth covered)
3 orientations of an igloo to consider as a PES:
Calculate for all Hazard Divisions
10 minutes for this work
From the side
From the front
From the back
MA05 Slide <number>
Notes: EXERCISE: (1 SLIDES, 20 MIN)
SLIDE 1 of 1: PART 2 (20 min)
(Instructor: You will now give the students another 10 minutes to do the calculations for Part 2 of the exercise).
You have identified that ESH 4 cannot be used for the HD 1.1. You want to try to get it all into a single ESH for the EOD teams.
You now decide to look properly at ESH 1, which was effectively your first choice anyway from gut feeling and intuition.
You will now take 10 minutes to calculate the QDs for ESH 1, using another blank ELL matrix. You need to calculate the QDs for all Hazard Divisions (ie not just 1.1!).
(Instructor: After their 10 minutes calculation time, or very slightly longer if the students only need an extra minute or so to complete their work, take the remaining 10 minutes of the session to review the students’ answers with them in a group.
Identify correct answers and explain why they are correct.
Identify whether or not the full stock of HD 1.1 stores in the manifest can be stored in ESH 1 (in terms of NEQ/QD, and also Units of Space) (Answer: Yes, as the ESH has a 1.1 NEQ maximum limit of 6,000kg, and there is only 596.85 kg of HD 1.1 on the manifest. There are 11 available UOS in the ESH, and there are currently 7 pallets/UOS on the manifest. This is useful as it may permit aggregation with other stores – in this scenario it won’t if the detonators are stored with the demolition charges, as this is aggregated to Compatibility Group F, according to the Mixing Rules, which require segregation from other possible stocks, unless Compatibility Group ‘S’ (as in the 1.4S ammunition) is collocated in this ESH. Alternatively, it offers significant extra capacity of HD 1.1 if the Equipment Table is ever increased, eg if an increased number of troops and/or tasks leads to an increase in the amount of ammunition and explosives that the deployed force requires).
Examine wrong answers further.
Ensure students fully grasp the principle of manual QD calculations by the end of the lesson.)
<number>

## Slide 6: End of Exercise
MA05 Slide <number>
Notes: (Instructor: Conclude the exercise session. Students need to have completed the full calculation of all HDs for ESH 1, or at least to hav grasped how to do it and to have a note of the permitted maximum NEQs for this ESH).
<number>