## Slide 1: Control of Explosive Facilities
MA8 Slide <number>
Notes: CONTROL OF EXPLOSIVE FACILITIES - INTRODUCTION: (1 SLIDE, 1 MIN)
SLIDE 1 of 1: INTRODUCTION (1 min)
Explosives facilities, by their very nature, present special hazards and these hazards must be uppermost in the minds of those responsible for their administration and who work in them.
In the event of an incident, the consequences could be severe. This may be in terms of severely inhibiting the defence capability, causing significant death and injury, and decimating the infrastructure around the site. This is particularly problematic where explosive facilities are located in the area of residential areas.
It is strongly recommended that the information contained in IATG 06:10 should be the minimum standard of national technical authority regulations in terms of control regimes for explosive facilities.
<number>

## Slide 2: Operational Procedures
Personnel to be Suitably Qualified and Experienced
Conditions of employment
Security
GENERIC CONTROLS
Will you go home ‘safe and sound’ at the end of every day?
MA8 Slide <number>
Notes: OPERATIONAL PROCEDURES: (8 SLIDES, 9 MIN)
SLIDE 1 of 8: OPERATIONAL PROCEDURES (2 min)
Some generic control requirements need to be applied to all explosive facilities.
(Instructor: click mouse now to reveal inner circle). The personnel employed to work in the facility should be properly trained and if necessary supervised. The technical term here is “Suitably Qualified and Experienced” or “SQEP” (pronounced skwep).
(Instructor: click mouse now to reveal inner circle). Careful consideration needs to be given to the specific conditions of employment for who is employed at the site, based on whether they are safe and capable. Particular consideration should be given to the disabled and to young people. IATG 06:10 gives further advice on these categories of staff.
People who are employed at the facilities need to be of sound body and mind. They must not be under the influence of alcohol or drugs.
(Instructor: click mouse now to reveal inner circle). Security is imperative and this topic will be covered later in the course. However the obvious requirements are a need for a security patrol, controlled access (eg using a swipe card or token system), enforcement of contraband rules, searching of personnel as required, the prohibition of flame, spark or heat producing items, vehicle tracker devices and so on.
This is an example of where a proper safety culture needs to be considered, rather than just doing a ‘tick box exercise’ and selecting workers and thinking that security is adequate.
Questions to ask yourself and your team:
Have you really got safe, competent, responsible people working in the facility?
Do they really know what not to do – and importantly what not to do?
Are the people actually capable of doing their job safely?
Is there a proper, manageable, workable access control system in place? Do you really know exactly who is in the site and where at any given point in time?
Have you really prevented prohibited items from entering the site?
(Instructor: click mouse now to reveal grey box).
In a nutshell – are you absolutely confident that if you had to spend a month working at the facility, that you would return home to your family and friends, safe, sound and in one piece, at the end of every day? If not, then you need to fix the causes of this doubt. You have a right to return home safe at the end of each day. So do your workers, no matter what level of seniority or pay they are at. The general public also have aright to go about their lives without being killed injured or having their lives and livelihoods destroyed.
<number>

## Slide 3: Operational Procedures
Controlled operations within PES:
  ESH / open bay storage
  Ready use ammunition
  Captured enemy / foreign ammunition
  Process buildings
MA8 Slide <number>
Notes: OPERATIONAL PROCEDURES: (8 SLIDES, 9 MIN)
SLIDE 2 of 8: OPERATIONAL PROCEDURES (1 min)
The operations that may be carried out in different types of PES must be strictly controlled.
This is because the consequences of an incident, particularly if, for example, sensitive items of ammunition are removed from their packaging for some reason within a site that is not properly set up for such work. The classic example is trying to conduct repair work on ammunition in an ESH when the rest of the stockpile within that ESH is still there. The likelihood of an incident is increased during such activities, and the NEQ of the surrounding stock may well be high. The mitigation measures to achieve an ALARP state will not be in place. This significantly increases risk. This kind of shortcut or carelessness must not happen.
Therefore, operations in PES are regulated.
The PES we will consider are:
ESH and open bay storage
Ready Use ammunition
Captured enemy ammunition and foreign explosives
Process buildings
<number>

## Slide 4: Operational Procedures
Cleaning – is acceptable
Key ‘rule of thumb’:
  Operations involving direct work on explosive articles and any exposure of explosives substances shall be strictly prohibited in Explosives Storehouses (ESH)
MA8 Slide <number>
Notes: OPERATIONAL PROCEDURES: (8 SLIDES, 9 MIN)
SLIDE 3 of 8: OPERATIONAL PROCEDURES (1 min)
Cleaning:
Of note, general cleaning activities like sweeping and dusting are usually acceptable in all PES types.
And the key ‘rule of thumb’ to this control:
Operations involving direct work on explosive articles and any exposure of explosives substances shall be strictly prohibited in explosives storehouses.
Other operations may be permitted within an ESH where movement of the store to a process area creates a greater risk. In such instances the head of the establishment may authorise such work. Each case shall be the subject of a full risk assessment. All other exceptions shall be referred to the national technical authority. However in general all other operations shall be carried out in process buildings.
What does all this mean? We can conduct munitions breakdown work in an appropriate APB. We must not however do this work in an ESH.
We can clean up in an ESH without removing all the stock, as long as it is appropriately packaged and any other mitigation measures are in place.
We would normally expect to move ammunition (in its containers) to an APB to do other work such as checking datalogger. However, if the risk of moving the stock is greater than the risk of doing this basic work in the ESH (As long as the containers aren’t opened), then this should be consider under a risk assessment, and in this case perhaps the datalogger work could be done in an ESH.
<number>

## Slide 5: ESH and Open Bay Storage
Permitted activities:
  Re-marking of packages
  Over-pack work, if packages within are sealed
  Opening Unit Load Containers to check humidity indicators
  Aircraft HE bombs in accordance with instructions – maintenance and inspection
  Visual inspection of aircraft weapons prepared for use
  Check temperature and humidity indicators/loggers if packages remain sealed
MA8 Slide <number>
Notes: OPERATIONAL PROCEDURES: (8 SLIDES, 9 MIN)
SLIDE 4 of 8: ESH AND OPEN BAY STORAGE (2 min)
The following operations may be permitted within a storehouse or open storage bay:
Re-stencilling and re-labelling of packages and unboxed stores
The build up and break down of weapon over-packs, ammunition containers and pallet configurations where the packages within are sealed or are unboxed stores
Opening unit load containers to check humidity indicators
The maintenance and inspection of aircraft high explosive (HE) bombs as long as the operations are carried out in accordance with instructions issued by the national technical authority
The visual inspection of prepared for use aircraft weapons
The checking of temperature and humidity indicators and approved data loggers as long as the check does not involve breaching containers or packages.
Low risk, short duration, tasks such as the repacking or visual inspection of a small quantity of ammunition may be permitted in the immediate vicinity of the parent licensed storage building at the discretion of the head of the establishment. This effectively means outside the building, albeit next to it. The doors to the parent building shall be closed. In this kind of activity, only one package (or two packages if fractioning ammunition for issue or storage) may be open at any one time.
<number>

## Slide 6: ESH and Open Bay Storage
Electronic Datalogger
MA8 Slide <number>
Notes: OPERATIONAL PROCEDURES: (8 SLIDES, 9 MIN)
SLIDE 5 of 8: ESH AND OPEN BAY STORAGE (no significant time on this slide)
The slide shows the fitting of an electronic datalogger to a munition. This may be done in an ESH (or open stack) as long as the packages themselves are not opened or the ammunition otherwise exposed.
<number>

## Slide 7: Ready Use Ammunition
The controls for ESH and open bays still apply.
However, if an APB is not reasonably practical:
  Issues / receipt / visual inspection may be done in a suitable area set aside for this purpose
  Risk assessment required
  Approval from National Technical Authority required
  Limited to Hazard Division (HD) 1.3 and 1.4 only
MA8 Slide <number>
Notes: OPERATIONAL PROCEDURES: (8 SLIDES, 9 MIN)
SLIDE 6 of 8: READY USE AMMUNITION (1 min)
In addition to the activities just mentioned for ESH and open bays storage:
If the use of a process building is not reasonably practical, then issues, receipts and visual inspection of ammunition may be conducted in a suitable area set aside for the purpose.
This task shall be subject to a written risk assessment having been carried out by the facility explosives safety representative. It should then be authorised by the national technical authority.
This activity shall be limited to stores of Hazard Division (HD) 1.3 and 1.4 only.
<number>

## Slide 8: Captured Enemy Ammunition and Foreign Explosives
Special regulations: IATG 06:10
Physical check by specialist
  Allocate HCC
  Confirm safe to store
Exception – ammunition purchased from foreign country if it is tested and has UN Serial Number
AIM – MINIMISE RISK POSED BY ‘UNKNOWN’ ITEMS
MA8 Slide <number>
Notes: OPERATIONAL PROCEDURES: (8 SLIDES, 9 MIN)
SLIDE 7 of 8: CAPTURED ENEMY AMMUNITION AND FOREIGN EXPLOSIVES (1 min)
Captured enemy and foreign explosives are subject to special regulations, as are improvised explosives recovered as part of Counter-Improvised Explosive Device (C-IED) operations.
There may be little available technical information about the explosives and ordnance. It is therefore necessary to define procedures to be adopted to ensure explosives safety is not compromised. IATG 06:10 covers this topic in more detail.
In summary though, the items should be physically checked by a technical specialist, and classified to allocate an Hazard Classification Code (HCC), and therefore to confirm it is safe for storage.
The risk must be minimised, for example the bare minimum of people are exposed to the item. Another risk mitigation measure is that this kind of ammunition should not be stored in any PES that also contains the national explosive assets.
The exception to this rule is ammunition which has been purchased from a foreign country, which has been qualified by the mandatory tests and has been allocated a UN serial number and compatibility grouping after testing as per the UN regulations shall be exempt from the above restrictions.
<number>

## Slide 9: Process Buildings
As previous requirements, but additionally:
  Separate Receipt and Issue Bay (R & I Bay)
  Special precautions: Electro Explosive Devices
MA8 Slide <number>
Notes: OPERATIONAL PROCEDURES: (8 SLIDES, 9 MIN)
SLIDE 8 of 8: PROCESS BUILDINGS (1 min)
These factors we have covered so far also obviously apply to APBs.
However, in addition, there should be a separate compartment within the building for receipt and issue (called an R and I Bay). Only the compartments authorised on the explosives licence shall be used for these activities. R&I bays may also be located in storage areas.
If EEDs or stores containing EEDs are handled, maintained, assembled, tested or prepared for use, RADHAZ Category 1 safe distances shall be applied. The earthing, conductive and antistatic and processing requirements given in IATG 05.40 Safety standards in electrical installations shall also be implemented.
<number>

## Slide 10: Estate Management
Site plans
Works services
Surplus facilities
Roads and drainage
Railway lines
Vermin control
Vegetation, crops, trees and shrubs
Livestock
MA8 Slide <number>
Notes: ESTATE MANAGEMENT: (1 SLIDES, 5 MIN)
SLIDE 1 of 1: ESTATE MANAGEMENT (5 min)
Good estate management is important in promoting the maintenance, safety and serviceability of PES and their contents.
In order to promote good estate management, heads of establishment need to liaise with the responsible authorities in order to ensure all appropriate measures are put in place.
Areas of responsibility need to be clearly defined.
The main areas to consider in estate management are:
Site plans. The head of the establishment shall ensure that accurate, scaled site plans are drawn up. These plans shall be held at the facility control office and by the fire focal point. Each PES shall be uniquely numbered to ease identification
Works services. Works services in, on or in the vicinity of a PES shall be carried out in accordance with IATG 06.60 Works services (construction and repair). This includes work such as keeping culverts and drainage clean, repairing damaged protective measures such as lightening protection, and so on.
Surplus facilities. The national regulations pertaining to explosives clearance and certification of surplus explosives facilities shall be followed. The regulations should ensure that all buildings and land are decontaminated and Certified as Free from Explosives (CFFE).
Roads and drainage. Roads in and leading to explosive facilities should be maintained in a good state of repair. This will lessen the risk of accidents. Drain covers in road surfaces should be serviceable and correctly fitted. Traffic flow systems should be clearly marked. Good drainage of the land in explosives facilities is essential to the proper maintenance of roads, railways and buildings. All streams, ditches and culverts should be kept clear and free of obstruction.
Railway lines. The head of the establishment should ensure that there is no obstruction to the view of road users or locomotive drivers at junctions of roads and railway lines. Warning notices should be prominently displayed at the approaches to all such junctions and the normal road traffic rules should be observed. If rail lines run between an explosives building and its associated traverse their use should be confined to traffic serving that building.
Vermin control. Vermin are a source of damage to buildings and services. Animals like rabbits and termites can cause severe damage to traverses and barricades, undermine buildings and roads, or damage ammunition and its associated packaging. Control measures should be taken to eliminate vermin and burrowing or boring animals from explosives facilities. However national legislation may protect some of these creatures as they may be ‘endangered or protected species’ and the head of the establishment should take note of any such legislation when considering solutions. Regular or periodical inspection should be carried out to ascertain any signs of attack or damage.
Vegetation and crops, trees and shrubs. This topic was covered in the lesson titled “Fire Safety and Contraband, C10”, and so will not be covered in more detail here. Note though that this is an important element of estate management.
Livestock. The grazing of livestock within explosives facilities should not normally be permitted. This is because of the amount of access time to the area normally required by the farmer or his or her employees and its consequential effect on the overall man limits and exposure time in the facility. However, should the head of the establishment consider such grazing feasible, a risk assessment should be carried out and the results submitted to the national technical authority for consideration. This shall be done before any contractual obligation is undertaken. Even if the livestock is the property of the facility the same procedure shall be followed.
<number>

## Slide 11: Aircraft Over Flight
Avoidance zones for aircraft under 1000m from ground level
Report persistent incursions
If explosive facility co-located at military airfield, enter details into aircraft standing orders to highlight the danger to pilots
MA8 Slide <number>
Notes: AIRCRAFT OVER FLIGHTS: (1 SLIDE, 3 MIN)
SLIDE 1 of 1: AIRCRAFT OVERFLIGHTS (3 min)
Major explosives areas shall be protected from the potential hazards of aircraft crashes by national technical authority measures, which shall designate these areas as avoidance zones.
These zones should preclude aircraft from over-flying such sites at heights of less than 1000m above ground level.
Persistent incursions of these avoidance zones should be reported to the national technical authority.
Local military air traffic at military airfields with explosives facilities is not generally restricted by such avoidance zones. In this case, the facility explosives safety representative should contact the senior air traffic control officer to request a suitable entry in the aircraft unit standing orders, which highlights the danger of potential disaster at large co-located explosives storage sites. In this way, aircrew can avoid such explosives facilities.
Conversely, explosives areas and facilities shall not be intentionally constructed in locations that would be over flown by existing or planned flight paths.
Some over flight by military helicopters may be acceptable, but these must be authorised in advance by the Head of Establishment after a proper risk assessment.
<number>

## Slide 12: Isolation and Segregation of Stocks
Banned or Constrained stock
Isolation of stock
Segregation of stock
MA8 Slide <number>
Notes: ISOLATION AND SEGREGATION OF STOCKS: (4 SLIDES, 6 MIN)
SLIDE 1 of 4: ISOLATION AND SEGREGATION OF STOCKS (1 min)
Ammunition and explosives which are known or suspected of being inefficient, unsafe, whose condition is uncertain, or which cannot be conditioned by the facility’s ammunition technical staff should be the subject of action in accordance with the instructions in IATG 01.70 Bans and constraints. It is likely that this will result in the banned or constrained stock being separated in some way or otherwise denoted as banned or constrained.
In addition, there may be requirements to otherwise isolate or segregate stocks.
<number>

## Slide 13: Isolation of Stock
Repairable or unserviceable stock that is suspected of being unsafe
Salvaged stores from accidents
Unsafe to use, but safe to store (eg some misfires)
EOD arisings
Experimental explosives (unsafe or unstable)
Upon instruction by appropriate authority
MA8 Slide <number>
Notes: ISOLATION AND SEGREGATION OF STOCKS: (4 SLIDES, 6 MIN)
SLIDE 2 of 4: ISOLATION OF STOCK (3 min)
Isolated storage is the storage of explosives which are in an unsafe or possibly unsafe condition. This should be in separate licensed storage away from all other explosives.
The following explosives should always be isolated:
Repairable or unserviceable explosives that are, or are suspected of being, unsafe
Salvaged stores recovered after an accident, explosion, fire or a trial
Explosive items which have failed to function and are unsafe for use, but not unsafe for storage. An example might be some types of misfired round.
Explosives recovered during explosive ordnance disposal (EOD) operations, (including foreign ammunition or improvised explosives) (called “EOD arisings”)
Experimental explosives that are determined to be unsafe or unstable
Any ammunition or explosives on the instruction of the national technical authority or other certified competent person
A PES which is to be used for the storage of explosives requiring isolated storage should be sited in such a location so as to afford all exposed sites (ES) the QD protection given by the tables in IATG 02.20 Quantity and separation distances. The use of reduced QDs shall not be permitted. Explosives requiring isolated storage should not normally be mixed by compatibility group. Explosives that require isolated storage should be addressed or disposed of as soon as
Practicable.
<number>

## Slide 14: Segregation of Stock
Methods of segregation:
  Separate compartment
  Internal traverse or barrier
  Physical distance
Internal Container Traverse in an ESH
MA8 Slide <number>
Notes: ISOLATION AND SEGREGATION OF STOCKS: (4 SLIDES, 6 MIN)
SLIDE 3 of 4: SEGREGATION OF STOCK (1 min)
Segregated storage is the storage of explosives whose compatibility groups, whilst not requiring separate storage, do not permit mixed storage.
The requirement for segregated storage may be met by any means which is effective in the prevention of propagation between the different groups, for example by a separate compartment, an internal traverse or barrier or by physical distance.
The normal mixing of compatibility groups is permitted for explosives requiring segregated storage.
(Instructor: click mouse to reveal image of a container traverse in an ESH, an example of an internal traverse or barrier)
<number>

## Slide 15: Segregation of Stock
Faulty but not unsafe
Experimental explosives
Enemy explosives
MA8 Slide <number>
Notes: ISOLATION AND SEGREGATION OF STOCKS: (4 SLIDES, 6 MIN)
SLIDE 4 of 4: SEGREGATION OF STOCK (1 min)
The following stores should always be segregated:
Stores known to be, or suspected of being, faulty but which are not unsafe
Experimental explosives
Enemy explosives
Again, this is to reduce the risk posed to the national ammunition stockpile, the explosive facility itself, and the people in and around the facility, both workers and non-associated civilians.
<number>

## Slide 16: Temperature Limitations - Background
Temperature °C
12.00
12.00
12.00
12.00
00.00
00.00
00.00
00.00
Time of day
Time of day
-10 5 0 5 10 15 20 25 30 35 40
Low diurnal cycle
High diurnal cycle
MA8 Slide <number>
Notes: TEMPERATURE LIMITATIONS: (3 SLIDES, 10 MIN)
SLIDE 1 of 3: TEMPERATURE LIMITATIONS - BACKGROUND (3 min)
In general explosives become less sensitive as the temperature drops.
However very low temperatures, high temperatures, or wide diurnal cycling may have an adverse affect upon the safety or function of ammunition.
For example, cracking of the explosives in an item of ammunition can occur which can affect its operation. In propellants, cracking can lead to increased burning rates and, in the extreme, detonation.
Nitro-glycerine freezes below 13 degrees C and may crystallize out. Should this happen, an increase in temperature may cause the leaching of nitro-glycerine.
High temperatures may cause exudation, expansion or increased decomposition rates. For example, TNT in the main charge of, say, an artillery shell may exudate at higher temperatures into the threads of the fuze well. In this case, it is possible that the TNT may detonate unexpectedly, particularly as the shell is fired in the gun.
<number>

## Slide 17: Temperature Limitations
Temperature limits
Minimum temperature
Maximum temperature
Record and monitor temperature using Max/Min Thermometers or dataloggers
Temperature is equally important during transportation
MA8 Slide <number>
Notes: TEMPERATURE LIMITATIONS: (3 SLIDES, 10 MIN)
SLIDE 2 of 3: TEMPERATURE LIMITATIONS (5 min)
The following restrictions should be considered when making major alterations to existing storehouses and when constructing new storehouses. They should be viewed as the ideal and a benchmark against which current capabilities are measured:
Temperature limits. When an ammunition or explosive item has more than one class of temperature restriction it shall be viewed as being in the class with the maximum restriction.
Minimum temperature. To prevent exudation of nitro-glycerine, nitrate ester-based propellants and articles containing such propellants should not be kept in storehouses for a continuous period of more than one month if the temperature in any part of the building is liable to remain below 5 degrees C. If the stipulated minimum temperature conditions cannot be sustained, artificial heating to an approved standard should be installed.
Maximum temperature. The efficiency, storage life and safety of some explosives, particularly propellants, are adversely affected by storage at abnormally high temperatures. They are not to be kept in storehouses where the temperature can be expected to rise above the limits shown in the national technical authority policy documents. The use of adequate ventilation, approved air conditioning, or insulation should be considered in order to keep temperatures in storehouses within approved limits.
Maximum and Minimum thermometers, or approved dataloggers, should be installed in buildings where ammunition which is susceptible to temperature is stored.
Temperature limitations are equally important during transportation.
<number>

## Slide 18: Maximum Temperature
Ammunition and explosives listed are to be stored in the coolest accommodation possible:
  Ammunition containing amatol or TNT
  Incendiary ammunition
  Propelling charges or ammunition containing propellants
  Ammunition containing WP or lachrymatory (tear producing) compositions
TNT which has been subjected to heat
MA8 Slide <number>
Notes: TEMPERATURE LIMITATIONS: (3 SLIDES, 10 MIN)
SLIDE 3 of 3: MAXIMUM LIMITATIONS (2 min)
Maximum temperature. The ammunition and explosives listed below are to be stored in the coolest accommodation possible:
Ammunition containing amatol or TNT
Incendiary ammunition
Propelling charges or ammunition containing propellants
Ammunition containing WP or lachrymatory (tear producing) compositions
<number>

## Slide 19: Moisture Protection and Ventilation
Humidity = moisture = damage to ammunition
  Seal and protect ammunition and explosives
  Ventilate only when Relative Humidity (RH) conditions are suitable
  Clear condensation through ventilation
  Use air dryers or air-con if necessary
  Do not open doors and windows as a means of routine ventilation
MA8 Slide <number>
Notes: MOISTURE PROTECTION AND VENTILATION: (1 SLIDE, 5 MIN)
SLIDE 1 of 1: MOISTURE PROTECTION AND VENTILATION (5 min)
Although proper ventilation is vital in a PES, indiscriminate admission of air into the PES may do more harm than good.
Proper sealing and protective coating of the ammunition and explosives and their associated packaging will offset some of the effects of moisture laden air.
For example:
On a warm day, the air is drier and better for ventilation than on a cold day. The reverse is also true. Therefore when the RH is high PES should not be opened for ventilation without first ascertaining that the conditions are suitable.
If condensation on the internal walls appears, use several ventilation periods to clear it.
In humid conditions normal ventilation may not be sufficient to keep condensation at an acceptable level. An air-drying or air conditioning apparatus (to an approved standard) may need to be installed.
In temperate climates PES ventilators should normally remain open and only be temporarily closed as an immediate precaution against the entry of rain or fog.
Note that ventilation by opening the doors and windows is not to be carried out unless condensation or excessive heat causes a problem.
Annex E to IATG 06:10 provides further details on ventilation equipment and procedures.
<number>

## Slide 20: Questions
MA8 Slide <number>
Notes: Are there any questions? 1 slide, 5 minutes
<number>